EXAMPLE 4

Instruction Memory’s file: 5th_fig456_MemEx4/inst.rom

This Mips pipeline implementation can handle branchs (with "nop" put by compiler) and forward data hazards

The user should set initial register values (linear). No data values are required.

Description: A simple sequence of five instructions with no data hazard.

ADD r1,r1,r1
SLT r2, r15, r1
BEQ r2,r0, -3
NOP
NOP

ADD r1,r1,r1 – type R instruction
opcode = 0 rs = 1 rt = 1 rd = 1 sh = 0 func = 32
000000 00001 00001 00001 00000 100000
0x00210820

SLT r2,r15,r1 – type R instruction
opcode = 0 rs = 15 rt = 1 rd = 2 sh = 0 func = 42
000000 01111 00001 00010 00000 101010
0x01E1102A

BEQ r2,r0,-3 – type I instruction
opcode = 4 rs = 2 rt = 0 imediate = -3
000100 00010 00000 1111111111111101
0x1040FFFD

NOP
0x00000000

NOP
0x00000000

The hexadecimal code example is:

ADD r1,r1,r1	– 0x00210820
SLT r2, r15, r1	– 0x01E1102A
BEQ r2,r0, -3	– 0x1040FFFD
NOP	– 0x00000000
NOP	– 0x00000000

Calculations check (with linear initial register values):

1. ADD r1,r1,r1	– R1 = 2
2. SLT r2, r15, r1	– R2 = 0
3. BEQ r2,r0, -3	– BACK TO THE FIRST INSTRUCTION
4. NOP
5. NOP
  1. ADD r1,r1,r1	– R1 = 4
  2. SLT r2, r15, r1	– R2 = 0
  3. BEQ r2,r0, -3	– BACK TO THE FIRST INSTRUCTION
  4. NOP
  5. NOP
    1. ADD r1,r1,r1	– R1 = 8
    2. SLT r2, r15, r1	– R2 = 0
    3. BEQ r2,r0, -3	– BACK TO THE FIRST INSTRUCTION
    4. NOP
    5. NOP
      1. ADD r1,r1,r1	– R1 = 16
      2. SLT r2, r15, r1	– R2 = 0
      3. BEQ r2,r0, -3	– BRANCH IS NOT TAKEN
      4. NOP
      5. NOP	– END.