EXAMPLE 2

Instruction Memory’s file: 5th_fig460_MemEx2/inst.rom

This Mips pipeline implementation can handle data hazards and cannot handle branchs.

The user should set initial register values (linear). No data values are required.

Description: A simple sequence of three “add” instructions with PIPE EXE data hazard.

ADD r2,r1,r3
ADD r3,r2,r1 //EXE HAZARD
ADD r1,r3,r2 //EXE HAZARD

ADD r2,r1,r3 – type R instruction
opcode = 0 rs = 1 rt = 3 rd = 2 sh = 0 func = 32
000000 00001 00011 00010 00000 100000
0x00231020

ADD r3,r2,r1 – type R instruction
opcode = 0 rs = 2 rt = 1 rd = 3 sh = 0 func = 32
000000 00010 00001 00011 00000 100000
0x00411820

ADD r1,r3,r2 – type R instruction
opcode = 0 rs = 3 rt = 2 rd = 1 sh = 0 func = 32
000000 00011 00010 00001 00000 100000
0x00620820

The hexadecimal code example is:

ADD r2,r1,r3 – 0x00231020
ADD r3,r2,r1 – 0x00411820
ADD r1,r3,r2 – 0x00620820

Calculations check (with linear initial register values):

ADD r2,r1,r3 – r2 = 4
ADD r3,r2,r1 – r3 = 5
ADD r1,r3,r2 – r1 = 9