EXAMPLE 1

Instruction Memory’s file: 5th_fig456_MemEx1/inst.rom

This Mips pipeline implementation can handle branchs (with "nop" put by compiler) and forward data hazards

The user should set initial register values (linear). No data values are required.

Description: A simple sequence of five “add” instructions with no hazards.

ADD r1,r1,r2
ADD r3,r0,r2
ADD r4,r0,r2
ADD r5,r0,r2
ADD r6,r0,r2

ADD r1,r1,r2 – type R instruction
opcode = 0 rs = 1 rt = 2 rd = 1 sh = 0 func = 32
000000 00001 00010 00001 00000 100000
0x00220820

ADD r3,r0,r2 – type R instruction
opcode = 0 rs = 0 rt = 2 rd = 3 sh = 0 func = 32
000000 00000 00010 00011 00000 100000
0x00021820

ADD r4,r0,r2 – type R instruction
opcode = 0 rs = 0 rt = 2 rd = 4 sh = 0 func = 32
000000 00000 00010 00100 00000 100000
0x00022020

ADD r5,r0,r2 – type R instruction
opcode = 0 rs = 0 rt = 2 rd = 5 sh = 0 func = 32
000000 00000 00010 00101 00000 100000
0x00022820

ADD r6,r0,r2 – type R instruction
opcode = 0 rs = 0 rt = 2 rd = 6 sh = 0 func = 32
000000 00000 00010 00110 00000 100000
0x00023020

The hexadecimal code example is:

ADD r1,r1,r2 – 0x00220820
ADD r3,r0,r2 – 0x00021820
ADD r4,r0,r2 – 0x00022020
ADD r5,r0,r2 – 0x00022820
ADD r6,r0,r2 – 0x00023020

Calculations check (with linear initial register values):

ADD r1,r1,r2 – r1 = 3
ADD r3,r0,r2 – r3 = 2
ADD r4,r0,r2 – r4 = 2
ADD r5,r0,r2 – r5 = 2
ADD r6,r0,r2 – r6 = 2