EXAMPLE 3

Instruction Memory’s file: 5th_fig456_MemEx3/inst.rom

This Mips pipeline implementation can handle branchs (with "nop" put by compiler) and forward data hazards

The user should set initial register values (linear). No data values are required.

Description: A simple sequence of three “add” instructions with PIPE MEM data hazard.

ADD r2,r1,r3
ADD r4,r4,r1
ADD r3,r2,r2

ADD r2,r1,r3 – type R instruction
opcode = 0 rs = 1 rt = 3 rd = 2 sh = 0 func = 32
000000 00001 00011 00010 00000 100000
0x00231020

ADD r4,r4,r1 – type R instruction
opcode = 0 rs = 4 rt = 1 rd = 4 sh = 0 func = 32
000000 00100 00001 00100 00000 100000
0x00812020

ADD r3,r2,r2 – type R instruction
opcode = 0 rs = 2 rt = 2 rd = 3 sh = 0 func = 32
000000 00010 00010 00011 00000 100000
0x00411820

The hexadecimal code example is:

ADD r2,r1,r3 – 0x00231020
ADD r3,r2,r1 – 0x00812020
ADD r1,r3,r2 – 0x00421820

Calculations check (with linear initial register values):

ADD r2,r1,r3 – r2 = 4
ADD r4,r4,r1 – r4 = 5
ADD r3,r2,r2 – r3 = 8