EXAMPLE 3

Instruction Memory’s file: 5th_fig460_MemEx3/inst.rom

This Mips pipeline implementation can handle data hazards and cannot handle branchs.

The user should set initial register values (linear). No data values are required.

Description: A simple sequence of three “add” instructions with PIPE MEM data hazard.

ADD r2,r1,r3
ADD r4,r4,r1
ADD r3,r2,r2 // MEM HAZARD

ADD r2,r1,r3 – type R instruction
opcode = 0 rs = 1 rt = 3 rd = 2 sh = 0 func = 32
000000 00001 00011 00010 00000 100000
0x00231020

ADD r4,r4,r1 – type R instruction
opcode = 0 rs = 4 rt = 1 rd = 4 sh = 0 func = 32
000000 00100 00001 00100 00000 100000
0x00812020

ADD r3,r2,r2 – type R instruction
opcode = 0 rs = 2 rt = 2 rd = 3 sh = 0 func = 32
000000 00010 00010 00011 00000 100000
0x00411820

The hexadecimal code example is:

ADD r2,r1,r3 – 0x00231020
ADD r3,r2,r1 – 0x00812020
ADD r1,r3,r2 – 0x00421820

Calculations check (with linear initial register values):

ADD r2,r1,r3 – r2 = 4
ADD r4,r4,r1 – r4 = 5
ADD r3,r2,r2 – r3 = 8